Barcode Scannner Quick Guide

1. Restore Factory Settings

Restore Factory Default (DF)

Note：After scan the “Restore factory default”, scans the right interface barcode of the barcode scanner

2. Interface Mode

RS232 (A0000)

*USB HID Keyboard (A0001)

RS485(A004)

3.Auto trigger(optional)

Disable Auto Trigger (H0000)

*Enable Auto Trigger (H0001)

4. Trigger Mode

*Single Read (F0000)

Continuous Read (F0001)

5.Read Mode

Disable Repeat Read (F0100)

*Enable Repeat Read (F0101)

Multiple Read（F0102）

6. Timeout Of Repeat Reading The Same Barcode

*0ms（F0200）

500ms（F0205）

1000ms（F0210）

7. Set suffix

*Disable suffix (J2000)

0x0D as suffix (J2001)

0x0D 0x0A as suffix (J2003)

Note：Note with “*” and bold fonts means factory default parameter

Single read: When a bar code has been decoded, the reader will be turned off. The reader must be triggered again to read label. It can be triggered via button, serial port or auto trigger.

Continuous read: The reader will produce as much data as it can decode regardless whether it is the same or not. This mode is mainly used for demonstration and diagnosis.

Disable repeat read: Disable continue to read the same barcode.

Enable repeat read: Enable continue to read the same barcode.

Multiple read: The same barcode can only be decoded again after the scanner leave and back to the same barcode.

Barcode Scanner

Quick  Guide

V1.1A

Number:75050028

# Text boxes

Reader setup process

①Scan “Enter Set”

Enter Set (%SET)

②Scan Function Barcode

③Scan “End & Save”

End & Save (%END)

Function Barcode

Barcode Function Instructions